## Slide 1: Lesson 1
Introduction to the Raspberry Shake
(adapted from Raspberryshake.org)

## Slide 2: What do we have here?

## Slide 3: The earth is always moving …even if we can’t feel it
We use the term SEISMIC
to describes ground motion,
or any vibrations of the
earth’s crust.
What are some examples of events that could cause ground motion?
Image - NASA

## Slide 4
Seismic events cause the release of energy outward in all directions
Like waves created
when a rock is
dropped into a pond
Ground motion waves are called
SEISMIC WAVES

## Slide 5
Seismic waves are released from the FOCUS of an earthquake.
They travel along the earth’s surface and through the earth’s interior
Area underground
where rocks moves
A Closer Look at Earthquakes
Image: EARTH SCIENCE, TARBUCK & LUTGENS, CHAPTER 8

## Slide 6: Measuring Seismic Waves
Just like we can measure sound waves with a microphone, we can measure seismic waves with a SEISMOGRAPH like the…
Seismographs record data with a suspended mass attached to a fixed base. When the earth shakes, the base moves and the mass does not.
Image: IRIS

## Slide 7
A SEISMOGRAPH is any device that detects and records seismic wave energy (ground vibrations)
They do not only measure earthquakes. All ground vibrations are “heard” by the sensors.
https://www.youtube.com/watch?v=DX5VXGmdnAg

## Slide 8: The Raspberry Shake Seismograph
Has 2 main components:
The geophone sensor
The digitizer and Raspberry Pi computer
Image: raspberryshake.net

## Slide 9
Turns ground movement into electrical current. More movement creates more current.
Converts to a digital signal we can see on our computer screen
Images: raspberryshake.net

## Slide 10: A seismograph produces a seismogram
Spectrogram
Seismogram
Notes: Seismogram – show ground motion (velocity) in meters/second over time (seconds in UTC)
Spectrogram – Shows frequency content of spectrogram. Represents the signal strength or ‘loudness’ over time

## Slide 11
It takes multiple seismographs to form a complete picture of a single earthquake!
MANY Raspberry Shakes around the world are monitoring ground motion and recording earthquakes
They are all connected through the Raspberry Shake Network

## Slide 12: The Raspberry Shake Network

## Slide 13: Practice: Explore the Raspberry Shake Network
Pick up a Raspberry Shake scavenger hunt worksheet from your teacher.
Go to…..https://stationview.raspberryshake.org/

## Slide 14: Why do you think it’s important to study earthquakes?
Notes: Discuss findings on Raspberry Shake Scavenger Hunt – lead into above question.
Why do you think it’s important to study earthquakes?
Look at the map closely. Where are we? What do you see?

## Slide 15
Tectonic plates are gigantic pieces of the Earth's crust and uppermost mantle (also called the lithosphere).
Image: NRCAN

## Slide 16
Getting To Know Tectonic Plates
Image: NRCAN

## Slide 17
DIVERGENT – moving apart
CONVERGENT – coming together
Subduction or Collision
TRANSFORM – move horizontally past each other
Image: Dillonfoster98.edublogs.org, 2014
Tectonic Plate Boundaries

## Slide 18
Can you find all 3 types of plate boundaries in this image?
1
2
3
Image: NRCAN

## Slide 19: Understanding how the earth moves is important
Earthquakes can be devastating but understanding them and knowing how to prepare for them can greatly reduce their risk
SEISMOLOGY is the study of seismic waves that travel through the earth.
A SEISMOLOGIST is a scientist who studies seismic events and helps engineers, architects and government to mitigate earthquake risks

## Slide 20: A school seismometer network and community science program
Run by seismologists at the University of Victoria and the Geological Survey of Canada, in partnership with the Hakai Institute.
Started deploying Raspberry Shake seismographs in 2022 to middle and high schools on Vancouver Island.
Data can be viewed through the Raspberry Shake website, or the Shakenet App.

## Slide 21
https://www.youtube.com/watch?v=fcuX1FTfeaA